## Slide 1: Street Light Automation and Fault Tolerance system
By: Harinarayanan K 2016115024
Stanley
Ashwin

## Slide 2: Abstract
28-33 % of electricity consumption by our state goes towards Street light lightning according to state reports. The present system is such that there is a single switch which controls many street light at once and the on/off of switch is controlled manually. The manual control is not perfect and leads to wastage of power. Our project is IOT based project which aims in automtion of this manual work and wireless control of street lamps based on Line of Sight.
The aim of the project is to minimize cost , monitor electricity consumption and faults on a regular basis and control all street lamps in real time from a central server.

## Slide 3: Structure of the system
The setup is such that there will be single microcontroller in control of a set of 10-15 street lamps each separated by 50m at least. Each of these microcontroller is in turn controlled by local server which will be present in the locality and further these local servers are controlled by a central server.

## Slide 4: Data communication and collection
Each of the street lamp will contain a NodeMCU containing an ESP8266 which will help in collecting data such as whether it is on or off , light intensity etc on regular interval.
The NodeMcu can work in two modes, Access point method ( AP) and station mode (ST) similar to client and server architecture.
Each of the NodeMCU can act as AP and ST to communicate with each other without need of internet , and data from each AP will be finall collected at the central microcontroller.

## Slide 5: Communication continued....
We have assumed that Internet connection will be available for the central microcontroller so that we send the data to local server using HTTP GET/POST methods.

## Slide 6: Drawbacks and Challenges
Using the communication model we have discussed , there pose a drawback in realtime because with thid model , there is a time lag between two nodeMCU when scanning for nearest Acces Point (AP) , which may lead to collection of data not at precise time .
Range coverage of microcontroller with other street lamps pose a challenge as we may require OMNI directional antenaaes which may cost heavily.

## Slide 7: Next MileStone
The next milestone to cover will be simulation of realtime implementation in a smaller scale without much attention to realtime synchronization but to ensure establishment of communication between ESP8266 devices.
This will be done using two NodeMCU's with a LED light and a sample server will be used to collect data and stored in backend with timestamp.

## Slide 8: Materials we have till now
1 arduino
2 nodemcu with esp8266
3 9v battery
3 relays
3 light sensors
1 current sensor
3 soldering boards
1 soler wire
soldering paste
3 small light bulbs with platforms
2 big light bulbs
2 breadboards
resistors,jumper wires and connecting wires